# Functional Test Record – SparkFun RedStick
Marshall Taylor
11/30/2015
HW version v01
## Verifying Serial Pinout
Procedure:
(note: Products that have TTL: FTDI basics, serial 7 segment, pi wedge)
List SparkFun Products with TTL serial port:
- FTDI basic
- Serial 7 segment
- Pi Wedge
- Serial LCD
- GPS modules

Criteria:
Do modern and useful serial ports line up properly more often then not? Discuss
No real standard exists. TX and RX are together on a lot, with various organizations of power and ground. The FTDI is the closest thing to standard but has extra pins. Going with any old 4 pin pattern really. This one allows reverse without shorting powers, but does let TXI drive ground.
## Power Circuitry Tests

#### Low Load Test
Procedure:
- Power from battery input with fine voltage supply.
- Increase input voltage from 1V to 6V. Measure Vin/Iin, Vout/Iout, ripple
Criteria:
- Does regulator provide clean output between 2.0 V and 5.0 V?
- Is efficiency above 80% in this range? No
- Is ripple below 10% in this range? Yes
- Mark the switching frequency: About 5kHz
- Data:

Ripple generated at low load (Burpy)
#### 100mA Load Test
Procedure:
- Load 100mA total, add load to VCC pin
- Power from battery input with fine voltage supply.
- Increase input voltage from 1V to 6V. Measure Vin/Iin, Vout/Iout, ripple

Criteria:
- Does regulator provide clean output between 2.0 V and 5.0 V? Yes
- Is efficiency above 80% in this range? No
- Is ripple below 10% in this range? Yes
- Mark the switching frequency: Various (See below)
- Data:

Ripple generated at 100mA
#### 200mA Load Test
Procedure:
- Load 200mA total, add load to VCC pin
- Power from battery input with fine voltage supply.
- Increase input voltage from 1V to 6V. Measure Vin/Iin, Vout/Iout, ripple

Criteria:
- Does regulator provide clean output between 2.0 V and 5.0 V? Voltage sags below 3.0 V, 4.0 V output at 2.5 V input
- Is efficiency above 80% in this range? No
- Is ripple below 10% in this range? Yes
- Mark the switching frequency: Various (See below)
- Data:

#### All Power Test Graphs

#### Test the regulator's reverse flow
Procedure:
- Apply 5.0 V to the serial VCC port
- Switch between shorting and opening the USB connection (simulate reverse plug-in)
Criteria:
The total current input should match the no-load consumption of the MPU +/- 5% Shorting the USB power lines had zero effect on current draw.
#### Test the battery protection from rogue VCC input
Procedure:
- Attach a 3.0 V battery and current meter to the battery input.
- Apply 5.0 V to the serial VCC port.
Criteria:
The battery must not accept current. The battery consumed 0.00 A
#### Test the battery protection from USB input
Procedure:
- Attach a 3.0 V battery and current meter to the battery input
- Apply 5.0 V to the USB VCC port
Criteria:
The battery must not accept current. The battery consumed 0.00 A
#### Extra test: Step loads
Procedure:
- Apply 2.5 V to the battery port
- Step loads between 0 and 100mA (total)
Criteria:
- Ringing should be minimal. 10 V for 40 ns
- Attach labeled scope captures.

38mA load switching in
75mA load switching in

75mA load switching out
95mA load switching in

95mA load switching out

#### Extra test: Reverse battery voltage
Procedure:
Apply reverse voltage to battery terminals
Criteria:
Must not crater. 0.00 A was consumed from the reverse voltage. RedStick operated normally afterwards.
## Set LED bias
Procedure:
- Measure red current at Vin = 2.0 V. 0.34mA
- Measure red current at Vin = 5.5 V. 0.36mA
- Measure green current at Vin = 2.0 V. 8.73mA
- Choose and set new resistors:
- Red: Use 4.7kOhm
- Green: Use 2.2kOhm for ~1.5mA of current
## Test I2C signal integrity
Procedure:
- Attach a I2C device and start communication
- Capture signals with a scope.
Criteria:
- Mark test device (AUT): 7segment display with 4.7kOhm pullups
- Are signals square and settled before clk edge?
- Clock should be clean
- Record scope capture

## Test SPI signal integrity
Procedure:
- Attach a SPI device through level shifter and start communication
- Capture signals with a scope between EUT and level shifter
Criteria:
- Mark test defice (AUT): BME280 with level shifter
- Are signals square and settled before clk edge?
- Clock should be clean
- Record scope capture

## Test serial TTL signal integrity
Procedure:
- Attach a serial device and start communication
- Capture signals with a scope.
Criteria:
- Mark test defice (AUT): FTDI loop at 115200 baud
- Are RX and TX typical?: Yes
- Record scope capture

TXO

RXI

## Test GPIO
Procedure:
- Set code to pulse each pin sequentially
- Capture signals with a scope.
- Look for out of order pulses ( > 1 pulse per pin13 cycle)
- Verify A0 – A7 by translating inputs to a PWM output and measuring
Criteria:
- Is each pin individually controllable? Yes
- Do any pins stick out as different from the others? No
- Do all analog inputs work and are stable? Yes
- Record scope capture of worst 2 pins. All pretty much the same