RedStick Review for Reds
Electrical Tests
Serial Port Ordering
Promotion through DigiKey

---
Voltage Under Load vs. Input Voltage

---
Battery protected from USB and VCC
Regulator stabilizes in ~40 ns
Reverse battery voltage OK
Runs 7x8 LED demo for 18 hr / 2 AA
I2C, SPI, UART, GPIO integrity OK
USB has nice fit

---
Serial Port Ordering
- Best standard is FTDI, not applicable
- 4 pin order selected

---
Changes from Proto
- Straightened Headers
- Re-biased LEDs
- Tweaked silkscreen

---
Promotion Through DigiKey
- (FYI Only) DigiKey is interested!
- Silk Mock-up: